## Slide 1
Smartphone IMU-Based
Real-Time
Posture Correction
Presented by
HyunJong Park
Mobile Computing and Its Application
Mini Project
Seoul National University
Spring 2026

## Slide 2
Goal & Usage Scenario
Detect poor neck posture during smartphone use
Problem
Users often maintain poor neck posture when using smartphones, which puts strain on the neck and can lead to neck pain and forward head posture.
Goal
Develop a lightweight, real-time posture correction system using only built-in smartphone IMU sensors (accelerometer & gyroscope) as an everyday posture-awareness assistant.
Usage Scenario
Standing
Sitting
Commuting

## Slide 3
Key Idea
Robust Posture Classification with Temporal Filtering
Input: 100 × 6 IMU window
(2 sec @ 50 Hz)
Lightweight 1D-CNN
Classes: Upright,
Mild Forward Flexion
Severe Looking-Down
Smooth prediction
probabilities
3-result moving average
Reduces transient
misclassification
8-sec sustained
poor-posture check
Vibration +
notification alert
Avoids immediate
false alarms
6-axis IMU input
50 Hz sampling
Ring-buffered sensor stream
Sense
Train
Infer
Feedback
 | t1 | t2 | t3 | avg
● | 0.60 | 0.40 | 0.55 | 0.52
● | 0.30 | 0.50 | 0.10 | 0.38
● | 0.10 | 0.10 | 0.10 | 0.10

## Slide 4
App Functionality Description
Posture Correction App – Screen Explanation
1
2
6
5
4
1. Model selection
Before starting monitoring, you can choose between INT8(default) or FP32(fallback)
2. Posture classification
Shows prediction for current posture (Upright, Mild Forward Flexion, and Severe Looking Down. )
Shows confidence for each state.
4. Monitoring status
Shows monitoring status: Stopped or Active
5. Latency
Shows inference latency of a model
6. Start/Stop monitoring
Button to start or stop monitoring
3. Countdown Bar
Shows countdown progress for persistent bad posture.
3

## Slide 5
App Functionality Description
Posture Correction App – Practical Features
Alert Rule
If bad posture continues for 8 seconds, the app sends a notification and vibration alert
Foreground Service
Runs a background service to track posture even when using other apps.
Screen-State Lifecycle Awareness
Automatically pauses sensor sampling when the screen turns off and resumes on screen unlock to save battery.
Adaptive Vibration Feedback
Vibration intensity and frequency vary depending on posture severity

## Slide 6
Comparison of Before/After Optimization
Improving Accuracy and Latency
Metric | Before Filtering | After Filtering
Test Accuracy | 90.72% | 92.90%
Macro F1 | 90.68% | 92.88%
Model | FP32 TFLite | INT8 TFLite
Size | 190 KB | 65KB
Latency | 0.1485ms | 0.1045ms
  Before (Raw Windows): 90.72% Accuracy, 90.68% Macro-F1. Slouching detection suffered from transitional noise.
  After (0.25s / 12-row margin removed): 92.90% Accuracy (+2.18%) and 92.88% Macro-F1 (+2.20%).
  Model Size: Achieved a ~66% size reduction for resource-constrained environments.
  Inference Latency: On invoke-only latency, the quantized INT8 model was 29.6% faster than the FP32 model on a Samsung Galaxy S23 Ultra.
Noisy Boundary Filtering
Model Quantization

## Slide 7
Project Timeline & Contribution
Full pipeline: collection to real-time inference
Handled the entire pipeline independently, from data collection to app implementation
Phase
1
Phase
2
Phase
3
Phase 4
Polish & Wrap-Up
  Polished minor features for practicality
  Prepared final demonstration materials.
On-Device Integration
  Developed the real-time posture monitoring App
  Integrated TFlite inference
Tooling & Data Collection
  Developed IMUDataCollectorApp for Android
  Collected 16 separate labeled CSV sessions (posture_session_*.csv) under various contexts
Preprocessing & Training
  Implemented preprocessing pipeline (50 Hz resampling, segmentation, transition margin trimming).
  Performed cross-session test split validation

## Slide 8
Thank You
https://github.com/13oris/PostureDetection

## Slide 9
App Functionality Description
IMU Data Collector App
1
2
3
4
5
1. Status
Shows the Session ID, Status of data collecting, Calibration status, and time elapsed for data collection
2. Calibration Button
Calibrates user’s natural upright position for 30 seconds
4. Context Selector
You can select three contexts(Standing, Sitting, Commuting) for data collecting
5. Label Selector
You can manually select 3 labels(Upright, Mild Forward Flexion, Severe Looking Down)
3. Start/Stop Button
Starts or stops data collecting